## Slide 1: DSCOVR Science Operations Center & EPIC Geolocation
Karin Blank
NASA/GSFC Code 586
October 31st, 2016

## Slide 2: Status
EPIC
  Reprocessing finished of version 01
  Public data released in July
NISTAR
  L1A/L1B processed
  L1A publically released in October
  L1B pending

## Slide 3: Upcoming
EPIC
  Version 02 (Winter)
    New flat fielding
    Stray light correction
    Updated geolocation
NISTAR
  Version 02

## Slide 4: Now Under New Management
Carl Hostetter (carl.f.hostetter@nasa.gov)

## Slide 5: Geolocation

## Slide 6: Algorithm Progress
Focus | Algorithm Version | Features
Simulator | Revision 0 | Pre-launch simulator
Relative Geolocation | Revision 1 | First geolocation; website pictures
 | Revision 2 | Mitigation of issues with optical artifacts
 | Revision 3 | Improved cross-band registration
 | Revision 4 | Subpixel registration L1b (Kai Yang’s algorithm)
Absolute Geolocation | Revision 5 | Initial fixes for absolution geolocation

## Slide 7
2D Model
2D Transform
3D Model
Input
Ephemerides
Time
Astronomical
Model
Ellipsoidal Model
View angles
Sun angles
Y transform
X transform
Registration
Ellipsoidal Coordinates
Geodetic coordinates
View angles
Sun angles
Instrument Model
L1A

## Slide 8
2D Model
2D Transform
3D Model
Input
Reference Geometry
Geodetic
coordinates
Image
Ellipsoidal Model
Ellipsoidal
Coordinates
Common Reference Grid
Per-image Angles
On Reference Grid
X transform
Y transform
Instrument Model
L1B

## Slide 9: Algorithm from revision 4 to 5

## Slide 10: Problem: Africa is too small
Credit: Dong Huang

## Slide 11: Projection size issue

## Slide 12: Focal Length
Focal length
Projection size

## Slide 13: Results
Manufacturer focal length: 286.2 cm
Estimated focal length: 283.82 cm
Difference: 2.38 cm

## Slide 14: Projection size after

## Slide 15: Problem: Inconsistent size
Issues
Error is lower in the center of projection and increases towards outer edges
Error is less along the equatorial axis than the polar axis
“Once you eliminate the impossible, whatever remains, no matter how improbable, must be the truth”
Sherlock Holmes (via Arthur Conan Doyle)

## Slide 16: 3D->2D transformation
Perspective Azimuthal Projection
  For space or aerial based photograph (photogrammetry)
  Accurate to e2
  2 formulations

## Slide 17: Perspective Azimuthal Projection

## Slide 18: Model effect

## Slide 19: “EPIC” Projection
Calculate XYZ coordinates for model using ellipsoid, geoid, & datum (ECEF)
Rotate model into EPIC’s reference frame
Convert to pixels by dynamically scaling each point as a function of…
  Distance
  EPIC’s perspective distortion (focal length effect)
  EPIC’s sensor format
Clip points outside of line of sight
Draw model
Notes: Earth Perspective, Includes Curvature

## Slide 20: Other changes
Anti-aliasing filter
  Reduce aliasing artifacts in 3D->2D transformation
Improved geoid model

## Slide 21: Future Revisions

## Slide 22: Refraction Correction

## Slide 23: Refraction Calculation
Simplified ray tracer (Hohenkerk & Sinclair)
  Stratosphere limit
  Stratosphere/Troposphere boundary
  Troposphere limit
Algorithm Input
  Viewing angle
  Wavelength
  Temperature
  Humidity
  Pressure
  Elevation

## Slide 24: Angular delta at different wavelengths
Refraction at 780nm
Refraction at 317nm

## Slide 25: Difference between 780nm and 317nm

## Slide 26: Future Work (r06)
Refraction correction
Backpropagation, part 1
  Time correction
Determining optical distortion (barrel/keystone)

## Slide 27: Future Work (r07)
Backpropagation, part 2
  Attitude correction
  Ephemeris correction?
Control point correction

## Slide 28: R04 results
Image with overlay
Error in pixels

## Slide 29: R05 results
Image with overlay
Error in pixels