## Slide 1
Development of a Science Quality Ocean Surface PAR Product from EPIC/DSCOVR Data (Update)
Robert Frouin, Jing Tan
Scripps Institution of Oceanography, University of California San Diego,
La Jolla, California
_____________________________________________________________________________________________________
DSCOVR Science Team Meeting, 6-8 October 2020

## Slide 2
Update
-Improved parameterization of atmospheric reflectance at large Sun and view zenith angles.
-Developed additional products, i.e., direct and diffuse PAR, PAR below surface, UV fluxes.
-Tested algorithm on many days; Compared monthly EPIC products with MODIS products.
-Code ready for production.

## Slide 3
Atmospheric Reflectance
-Quasi-single scattering approximation was used; but does not work well at large Sun and view angles (actual reflectance is overestimated).
-New parameterization combines exact single scattering and quasi-single scattering approximations:
Ra = fSS(m, taer) RaSS + fQSS(m, taer) RaQSS
where m is air mass and taer aerosol optical thickness at 550 nm. Unique f functions for all aerosol models.
-Edge effects in daily PAR product are eliminated with new parameterization.

## Slide 4
𝜏aer=0.4, 388 nm
𝜏aer=0.4, 551 nm
𝜏aer=0.2, 551 nm
𝜏aer=0.2, 388 nm
Ra parameterization, SCAT = 171.5 deg., SZA = 60 deg., Maritime aerosols
Modeled
SS
QSS
“Exact”

## Slide 5
𝜏aer=0.4, 388 nm
𝜏aer=0.4, 551 nm
𝜏aer=0.2, 551 nm
𝜏aer=0.2, 388 nm
Modeled
SS
QSS
“Exact”
Ra parameterization, SCAT = 171.5 deg., SZA = 75 deg., Maritime aerosols

## Slide 6
Daily mean PAR, January 1, 2018, obtained using EPIC imagery at 00:17:51 UTC with new and old Ra parameterizations (SZA<85 deg.; VZA<75 deg.)
Old
New
Daily mean PAR reduced by -1.4 E/m2/day on average (3.6%) with new Ra parameterization.

## Slide 7
Radiation Products Suite
-Daily mean downwelling PAR just above ocean surface (E/m2/Day) Basic product
-Daily mean direct downwelling PAR just above ocean surface (E/m2/Day)
-Daily mean diffuse downwelling PAR just above ocean surface (E/m2/Day)
-Daily mean downwelling PAR just below ocean surface (E/m2/Day)
-Daily mean downwelling UV flux at 340 nm just above ocean surface (mW/cm2/µm)
-Daily mean downwelling UV flux at 388 nm just above ocean surface (mW/cm2/µm)
-All products are generated on both Plate Carrée (18.4 km resolution at Equator) and equal-area (18.4 km resolution) grids compatible with those of NASA OBPG ocean color products.

## Slide 8
EPIC Daily mean PAR just above surface, July 1, 2018
EPIC Daily mean PAR just below surface, July 1, 2018

## Slide 9
EPIC Daily mean direct PAR just above surface, July 1, 2018
EPIC Daily mean diffuse PAR just below surface, July 1, 2018

## Slide 10
EPIC Daily mean UV(340 nm) flux just above surface, July 1, 2018
EPIC Daily mean UV(388 nm) flux just below surface, July 1, 2018

## Slide 11
Comparison between EPIC and MODIS-A daily mean PAR(0+), July 1, 2018
EPIC
MODIS-A
Difference (EPIC – MODIS)
R2 = 0.926
Bias = -2.8(9.1%)
E/m2/day
RMSD = 6.1(20.0%)
E/m2/Day

## Slide 12
R2 = 0.978
Bias = -2.8(7.1%) E/m2/day
RMSD = 3.5(8.9%) E/m2/Day
EPIC - MODIS
EPIC
MODIS-A
Comparison between EPIC and MODIS-A monthly mean PAR(0+), October 2018
EPIC PAR field less noisy
EPIC PAR range larger
EPIC values lower

## Slide 13
Future Work
-Production/release of daily mean PAR products (+ATBD).
-Further evaluation (LEO and GEO estimates, in-situ measurements, RT model simulations with spherical-shell atmosphere) and quality checks.
-Association of uncertainties (bias, standard deviation) to each grid point.
•Simulations of noisy EPIC measurements and corresponding surface
fluxes for wide range of situations (MERRA-2, SMART-G code)
•Parameterization as a function of clear sky value and cloud factor
•GAM with varying coefficients depending on geographic location,
day of year, auxiliary variables.