## Slide 1
CONOPS for a Lunar observatory vs EPIC/DSCOVR
Nick Gorkavyi (SSAI)
Reference
A. Marshak, N. Krotkov, N. Gorkavyi, S. Marchenko, A. Vasilkov, Y. Knyazikhin, M. Kowalewski, O. Torres, M. DeLand, M. Ramsey, P. Christensen, V. Realmuto “Whole Earth imaging from the Moon South Pole (EPIC-Moon)” White Paper for ROSES-2021 (Artemis program)
The DSCOVR/EPIC imager observs the entire sun-illuminated Earth from the Lagrange L1 point. The L1 location, however, restricts the phase angles to ~2o-12o, a nearly backscattering direction, depriving the observer of any information about the bidirectional surface reflectance factor (BRF) and/or a cloud/aerosol phase function. A compact, lightweight, autonomic camera on the Moon’s surface offers unique opportunity to overcome these limitations and advance Earth science in ways difficult to predict.
DSCOVR EPIC and NISTAR STM
October 6-8, 2020 (Virtual)

## Slide 2
December 22
June 22
September 22, 2020
Seasonal variation of Earth from EPIC view
Figure 1. The phase angle or Solar-Earth-Vehicle (SEV) will be same for all seasons and for all illuminated surface of the Earth.

## Slide 3
Figure 2. Solar-Earth-Vehicle
(SEV) for DSCOVR/EPIC vary from 2 to 12 deg.
Phase angle
or SEV
Phase angle or Solar-Earth-Vehicle (SEV)

## Slide 4
23.4°
5.145º
N
R=(362.6–406.7)*103 km
150*106 km
Synodic lunar month 29.53 day
A
B
C
D
E
3.7 day
EPIC
SIDE VIEW
TOP VIEW
EPIC
Sun-Earth-Moon-system
Eccentricity
=0.0549
N
1.5º
Fig. 3. General view of the
Sun-Earth-Moon system

## Slide 5
Figure 4. Top view and a view from Moon for phase angle 45 deg.
Phase angle or Solar-Earth-Vehicle (SEV)=45 deg
TOP VIEW
Point B: 3.7 day after new Moon = full Earth
Earth
Moon
SEV=45°
https://www.youtube.com/watch?v=eV1ZXm3MH6I
Credit for view from Moon: James O’Donoghue and PhysicsJ
“How Earth looks from the Moon… during April 2020”

## Slide 6
TOP VIEW
Phase angle or Solar-Earth-Vehicle (SEV)=90 deg
Point C: 7.4 day after new Moon
SEV=90°
Figure 5. Top view and a view from Moon for phase angle 90 deg. Adding TIR camera would allow continuous 24 hour whole Earth observations.
Credit for view from Moon: James O’Donoghue and PhysicsJ

## Slide 7
TOP VIEW
Phase angle or Solar-Earth-Vehicle (SEV)=135 deg
Point D: 11.1 day after new Moon
SEV=135°
Figure 6. Top view and a view from Moon for phase angle 135 deg.
Credit for view from Moon: James O’Donoghue and PhysicsJ

## Slide 8
TOP VIEW
Phase angle or Solar-Earth-Vehicle (SEV)=180 deg
Point E: 14.8 day after new Moon = full Moon
SEV=180°
Figure 7. Top view and a view from Moon for phase angle 180 deg.
Credit for view from Moon: James O’Donoghue and PhysicsJ

## Slide 9
0 7 14 21 28 Days
180°
0°
90°
EPIC SEV
angular range
SEV for Moon
Observatory
Fig.8 Phase angle or Solar-Earth-Vehicle angle for any daylight Earth’s object
from the Artemis location near Moon South Pole during lunar month,
compared to the EPIC’s 2o-12o yearly range.

## Slide 10
S
20 km
Lunar south pole
Rim of Shackleton crater
(NASA/GSFC/Arizona State University)
Shackleton crater
Three points on the rim remain
collectively sunlit for more than
90% of the year

## Slide 11
Figure 9. A view from Lunar south pole. For observer in equatorial lunar area the Earth will be in the zenith. (Photo of surface of the Moon: NASA/Apollon; View from Moon: James O’Donoghue)
S
N
The Sun will be under horizon
~ 10% of the year

## Slide 12
Earth science goals for a Lunar observatory:
The combination of UV-TIR imaging from the lunar surface will allow:
comprehensive (both in time and space, compared to LEO) whole-globe monitoring of transient volcanic and aerosol clouds (smoke, dust), including the strategically important for climate studies polar regions not covered by GEO missions;
simultaneous imaging of the day and night parts (thus, the twilight zone);
better detection of circum-polar, high-altitude clouds (PMC) via the whole-Earth limb imaging;
subpixel image processing, allowing ~1 km vertical resolution of stratospheric aerosol limb profiles synergistically with ESD LEO missions: SNPP/OMPS-LP and ISS/SAGE-III;
monitoring of the vegetation characteristics and plant physiology (BRF), as well as vegetation stress and evapotranspiration (TIR channel), thus contributing to the global carbon cycle studies;
better (full phase-angle integrated) surface albedo estimates.

## Slide 13
Lunar environment goals for a Lunar observatory:
The lunar dust exosphere is an important factor for the long-term stay of astronauts on the Moon, as well as for the functioning of scientific equipment on the moon surface and orbiters. Telescopic limb observations of the scattering of sunlight (or starlight) from a lunar dust cloud should help build a 3D model of the lunar dust exosphere.
Using the Earth's atmosphere as a detector, the EPIC-Moon imaging of night-side as well as limb of the Earth will detect atmospheric impacts (either by a flash or dispersion of meteoritic dust clouds) from the potentially threatening small (<10 m) asteroids in the circum-Earth space, thus improving the current highly uncertain estimates.