## Slide 1: Status of Ozone products from the DSCOVR EPIC Instrument
Natalya Kramarova1, Liang-Kang Huang2, Jerald R. Ziemke3, Jay Herman4 , David P. Haffner2, Gordon Labow2 ,Richard D. McPeters1, P.K. Bhartia1, and Luke Oman1
1NASA Goddard Space Flight Center, Greenbelt, MD
2Science Systems and Applications Incorporated, Lanham, MD
3Morgan State University, Baltimore, MD
4University of Maryland Baltimore County, MD
DSCOVR Science Team Meeting, October 6-8, 2020

## Slide 2
DSCOVR Science Team Meeting, October 6-8, 2020
The retrieval algorithm is based on EPIC version 2 [Herman et al, 2018] with few modifications:
Triplet 318 nm, 340 nm & 388 nm at low optical path (<1.5)
or 325 nm, 340 nm & 388 nm at high optical path
Reflectivity is based on 388 nm and changes linearly with wavelength;
Ozone absorption cross sections from Brion, Daumont, Malicet [1995];
Algorithm uses LUT based on TOMRAD: 26 ozone profiles (V8 SBUV climatology), 4 pressure levels [1.00, 0.70,0.40,0.20], 10 Solar Zenith Angles [0,30,45,60,70,77,81,84,86,88], and 11 Satellite View Angles [0,15,30,45,60,70,77,81,84,86,88].
EPIC Total Ozone version 3

## Slide 3
DSCOVR Science Team Meeting, October 6-8, 2020
Modifications in version 3:
Switch to Version 3 Level 1 product that includes:
  Improved geolocations (~ 1 CCD pixel) ==> improved Solar/View Angles;
  Improved Flat Field Calibrations for UV channels (~0.5%) ;
  New Dark Counts Correction for UV channels.
Switch to the cloud height product from EPIC A-Band to replaced OMI-based cloud height climatology (hybrid approach: if EPIC A-band not available then climatological height is used);
Update absolute calibrations using polar orbiting SNPP OMPS (static correction);
Added corrections for ozone profile shape and temperature;
Update algorithm flags to filter data;
Added column weighting functions for each observation.
EPIC Total Ozone version 3

## Slide 4
DSCOVR Science Team Meeting, October 6-8, 2020
EPIC Total Ozone version 3
EPIC A-band cloud retrievals: [Yang et al, 2019]
With cloud climatology
With A-band cloud product
Improvements due to switch to simultaneous cloud height retrievals from EPIC A-band

## Slide 5
Synoptic ozone maps: EPIC v3 and MERRA-2
DSCOVR Science Team Meeting, October 6-8, 2020
Notes: EPIC map is noisier than MERRA-2. Are these small structures artifacts of EPIC measurements or real geophysical noise? How we can determine that?

## Slide 6
DSCOVR Science Team Meeting, October 6-8, 2020
EPIC Total Ozone v3 vs SNPP OMPS NM v2.1

## Slide 7: 20oN-60oN, 25 April 2017
All Clouds
Cloud Free
DSCOVR Science Team Meeting, October 6-8, 2020
EPIC Total Ozone v3 vs SNPP OMPS NM v2.1

## Slide 8: 20oS-20oN, 25 April 2017
All Clouds
Cloud Free
DSCOVR Science Team Meeting, October 6-8, 2020
EPIC Total Ozone v3 vs SNPP OMPS NM v2.1

## Slide 9: 20oS-60oS, 25 April 2017
All Clouds
Cloud Free
DSCOVR Science Team Meeting, October 6-8, 2020
EPIC Total Ozone v3 vs SNPP OMPS NM v2.1

## Slide 10
EPIC: Satellite
View Angles
< 70o
EPIC: Uses all
AlgorithmFlag and
ErrorFlag filtering
DSCOVR Science Team Meeting, October 6-8, 2020
Agreement within +/- 5 DU or ~ +/-2%
EPIC Total Ozone version 3 vs OMPS, OMI and MERRA-2

## Slide 11
EPIC Total Ozone v3 vs ground-based Brewer network
DSCOVR Science Team Meeting, October 6-8, 2020

## Slide 12
DSCOVR Science Team Meeting, October 6-8, 2020
EPIC Total Ozone v3 vs ground-based Brewer network

## Slide 13
DSCOVR Science Team Meeting, October 6-8, 2020
UV measurements have reduced sensitivity to the boundary layer;
CWFs represent the weight of measurements in the boundary layer;
CWFs are determined by Jacobians (or sensitivity of measurements to O3 changes in the lower layers);
Important for tropospheric ozone product.
EPIC Total Ozone v3: Column Weighting Functions
Notes: CWF depend on:
Terrain height
Viewing geometry
Surface reflectivity/cloud height

## Slide 14
EPIC: Satellite View Angles < 70o
DSCOVR Science Team Meeting, October 6-8, 2020
EPIC Reflectivity and CFW
Notes: CWF depend on:
Terrain height
Viewing geometry
Surface reflectivity/cloud height

## Slide 15
EPIC: Satellite View Angles < 70o
DSCOVR Science Team Meeting, October 6-8, 2020
EPIC CFW and A-Band cloud height

## Slide 16
Correlative ozone measurements for EPIC’s validation
 | External Measurements | Validated EPIC Products
Satellite | Aura OMI, SNPP OMPS | Total Column
Ground-based | Ozone sonde (SHADOZ, NDACC, WOUDC) | Tropospheric profile/ Column
 | Brewer/Dobson, Pandora | Total Column
 | Tropospheric lidars | Tropospheric profile/ Column
Aircraft | Atmospheric Tomography (ATom) Missions (ATom-1: July-August 2016, ATom-2: Jan-Feb 2017, ATom-3: October 2017, ATom-4: April-May 2018) | Tropospheric profile/ Column
Model | GEOS-Replay | Tropospheric profile/ Column
DSCOVR Science Team Meeting, October 6-8, 2020

## Slide 17
DSCOVR Science Team Meeting, October 6-8, 2020
EPIC v3 total ozone data had been processed and released to DAAC;
Comparisons of EPIC’s total ozone with overlapping satellite instruments (SNPP OMPS and Aura OMI) demonstrated a good agreement with ±5 DU or ±1.5-2%;
Biases in ozone are smaller at equatorial latitudes and increase in mid- and high latitudes, where biases vary seasonally;
No apparent biases in total ozone due to switch to EPIC A-Band cloud product;
There are still larger biases for EPIC measurements at high angles (SZA/SVA). In our study we limit SZA/SVA <70;
Comparisons with ground-based Brewer network are consistent with satellite results.
Summary

## Slide 18
DSCOVR Science Team Meeting, October 6-8, 2020
Prepare and release a User Guide for EPIC’s total ozone v3 to describe reported data, error flags and summarize data quality;
Validate EPIC’s tropospheric ozone maps using various ground-base and aircraft measurements and model simulations;
Publish a paper that summarizes validation results for v3 EPIC total and tropospheric ozone products;
Prepare and release synoptic and daily tropospheric ozone maps.
Future work

## Slide 19
DSCOVR Science Team Meeting, October 6-8, 2020
EPIC total ozone data are available at:
https://epic.gsfc.nasa.gov/science/products/o3
https://cmr.earthdata.nasa.gov/search/concepts/C1707836925-LARC_ASDC.html
EPIC Total Ozone version 3
Notes: Summarize all flags, pixel averaging etc. that is relevant to the following analysis.