## Slide 1: Improvement of SO2 Algorithm and Validation of Total O3 from DSCOVR EPIC
Kai Yang – UMCP
DSCOVR Science Team Meeting
October 6 – 8, 2020

## Slide 2: Algorithm improvement: Background and Motivation
EPIC often provides multiple observations of volcanic clouds in a day and frequently captures the fresh clouds during or soon after eruptions.
Fresh volcanic clouds often contain both gases and ash particles injected into the atmosphere during eruptions.
The estimation of ash mass loading, in addition to the amount of SO2, provides critical information for the study of the temporal evolution of a volcanic plume.
The presence of aerosols complicates the modeling scattered light paths required by the retrieval algorithm, leading to large uncertainty in SO2 quantification.

## Slide 3: Volcanic Plume example: Raikoke Eruption True Color Image from Terra MODIS on 06/22/ 2019
Fresh volcanic plumes often contain large amount of ash.
Notes: ﻿The Moderate Resolution Imaging Spectroradiometer (MODIS) on NASA’s Terra satellite acquired the second image on the morning of June 22. At the time, the most concentrated ash was on the western edge of the plume, above Raikoke. The

## Slide 4: Simultaneous Quantification of Volcanic SO2 and Ash
Ash cloud model: mixture of ash particles and water/ice clouds, replacing the MLER treatment of elevated particles
Estimation of ash single scattering albedo and optical depth from long wavelength UV bands.
Extending the single scattering albedo and optical depth to short UV bands based on the ash cloud model.
Retrieval of O3 and SO2 amounts, with radiative transfer modeling of particle laden atmosphere to match radiance measurements from short UV bands.

## Slide 5
Quantification of Volcanic Ash
Ash Mass Concentration (g/m2)
Volcanic Cloud: Mixtures of Water/Ice Clouds and Ash Particles
Micro-physical properties of each component:
Particle shape (e.g. sphere/spheroid/irregular), mass density (e.g, ρash=2.75 g/cm3)
Size distribution (e.g., Log-normal for ash particles, reff = 2μm, σ=1.6),
Refractive index (e.g. real = 1.5, imag = 0.005, independent of λ)
Volcanic Cloud: Optical Properties
Mass Coefficients: Scattering (Ksca), Absorption (Kabs),
Extinction (Kext=Ksca+Kabs), Single Scattering Albedo (ω0=Ksca/Kext),
and Scattering Phase Function
Vertical Distribution of Particles:
Layer height estimated from radiance measurements or trajectory analysis
Surface Albedo
Estimated from radiance measurements or based on climatology
Extinction Optical Depths for Each Components: estimated from satellite radiance spectra
Model and Mie Calculations
Measurements and Retrievals

## Slide 6
The ratio of EPIC band 3 - band 4 radiances as a function of band 4 radiance, calculated for different fractions of cloud and ash mixture, with optical properties determined from the microphysical properties
SZA=45° VZA=0° surface reflectivity = 0.1 Ash layer height = 4 km
Pure water cloud ωw = 1 pure ash ωa = 0.63.
Ash cloud estimation:
single scattering albedo (ω) and optical thickness (τ)

## Slide 7: Examples from EPIC observations
Eruption of Etna (Italy) on December 3, 2015
Eruption of ﻿Ambae (Vanuatu) on July 26, 2018
Eruption of Raikoke (Kuril Islands) June 22-23, 2019

## Slide 8: Eruption of Etna (Italy) on December 3, 2015 Aerosol Optical Depth
AOD

## Slide 9: Eruption of Etna (Italy) on December 3, 2015 Single Scattering Albedo
SSA

## Slide 10: Eruption of Etna (Italy) on December 3, 2015 SO2 Column Amount
SO2
(DU)

## Slide 11: Eruption of ﻿Ambae (Vanuatu) on July 26, 2018 Aerosol Optical Depth
AOD

## Slide 12: Eruption of ﻿Ambae (Vanuatu) on July 26, 2018 Single Scattering Albedo
SSA

## Slide 13: Eruption of ﻿Ambae (Vanuatu) on July 26, 2018 SO2 Column Amount
SO2
(DU)

## Slide 14: Eruption of Raikoke (Kuril Islands) June 22-23, 2019 Aerosol Optical Depth
AOD

## Slide 15: Eruption of Raikoke (Kuril Islands) June 22-23, 2019 Single Scattering Albedo
SSA

## Slide 16: Eruption of Raikoke (Kuril Islands) June 22-23, 2019 SO2 Column Amount
SO2
(DU)

## Slide 17: Summary of SO2 Improvements
Explicit treatment of aerosol allow direct quantification of ash optical loading and optical properties from UV spectral measurements.
Simultaneous quantification volcanic SO2 and ash greatly improve the accuracy of gas (O3 and SO2) retrievals.

## Slide 18: Update Ozone Algorithm for V3 processing
Replacing climatological cloud pressure with EPIC cloud pressure product.
Update O3 profile climatology to include spatial dependence, more accurate representation of tropospheric O3 (see Yang and Liu, 2019, https://doi.org/10.5194/amt-12-4745-2019)

## Slide 19: Ozone Validation with Brewer Measurements
Station Name | Latitude
Alter | 82.50
Eureka | 79.99
Resolute | 74.72
Churchill | 58.75
Edmonton | 53.55
Goose Bay | 53.31
De Bilt | 52.10
Thessaloniki | 40.63
Paramaribo | 5.806
South Pole | -89.99

## Slide 20: High Northern Latitude

## Slide 21: High-Mid Northern Latitude

## Slide 22: Mid Northern Latitude

## Slide 23: Low Northern Latitude

## Slide 24: South Pole

## Slide 25: V3 EPIC Total O3 Validation Summary
Time series of O3 difference between coincident EPIC and Brewer and EPIC and MERRA-2 are stable with similar moving average and standard deviation, showing EPIC O3 are consistent over time, without noticeable drift.
The correlations between EPIC and Brewer (R>0.87) and EPIC and MERRA-2 (R>0.92) are high, demonstrating that EPIC captures the dynamical variability accurately. V3 has higher correlation and lower standard deviation with Brewers than V2.
Against Brewer data, EPIC O3 has latitude dependent biases, which increases towards the poles. V3 has higher biases than V2, which exhibits less latitude dependence.
Calibration adjustments are expected to reduce biases against Brewers and will be developed for reprocessing and release of V3 O3SO2AI product.