## Slide 1: Validation and Comparison of Total O3 and Volcanic SO2 from DSCOVR EPIC
Kai Yang - UMCP
DSCOVR Science Team Meeting
GSFC Sept. 17 – 18, 2018
Acknowledgement: This work is supported by NASA.

## Slide 2: EPIC O3 and SO2 Product O3SO2AI Released
Direct Vertical Column Fitting (DVCF) Algorithm
O3SO2AI: O3, LER, and AI
Synoptic view of the sunlit Earth on October 3, 2016 at 12:54:13 UTC.
O3
LER 340 nm
AI

## Slide 3: EPIC O3 and SO2 Product O3SO2AI Released
O3SO2AI – EPIC SO2 retrieved using DVCF algorithm.
Volcanic SO2 plumes from the eruption of Kilauea volcano in Hawaii on June 22 – 23, 2018. A series of SO2 spatial maps are obtained about 65 minutes apart.

## Slide 4: Validation and Comparison: Total O3
Validate the DVCF O3 retrievals from EPIC using coincident ground-based Brewer spectrophotometer measurements and the assimilated O3 product from MERRA-2.

## Slide 5: ﻿Coincident Measurements: EPIC, MERRA-2, Brewer
Notes: Large O3 range: 220 – 520 DU, 300 DU range, Brewer and Merra-2 data are interpolated to the time EPIC observations; All three independent data set track each other well.

## Slide 6: ﻿EPIC O3 Validation: EPIC vs. Brewer
ΔO3 = EPIC – Brewer | VZA < 69°
﻿ –1.18 ± 3.05% or –4.19 ± 10.50 DU
R = 0.97

## Slide 7: ﻿EPIC O3 Validation: EPIC vs. MERRA-2
ΔO3 = EPIC – MERRA-2 | VZA < 69°
﻿ 0.65 ± 2.39% or 2.13 ± 7.91 DU
R = 0.98

## Slide 8: ﻿EPIC O3 Validation: MERRA-2 vs. Brewer
ΔO3 = MERRA-2 – Brewer | VZA < 69°
﻿ –1.80 ± 2.52% or –6.35 ± 8.90 DU
R = 0.98

## Slide 9: Summary Coincident O3 Comparisons
Biases
  EPIC vs. Brewer : bias low by 1.18% or 4.19 DU
  MERRA-2 vs. Brewer: bias low by 1.80% or 6.35 DU
  EPIC vs. MERRA-2 : bias high by 0.65% or 2.13 DU
  * EPIC bias may be easily adjusted with soft calibration
Standard Deviation and Correlation
  EPIC vs. Brewer : std = 3.05%, R = 0.97 |Worst
  MERRA-2 vs. Brewer: std = 2.52%, R = 0.98 | Very good
  EPIC vs. MERRA-2 : std = 2.39%, R = 0.98 |Best
MERRA-2 contains realistic O3 field, though it likely biases low by ~1.5%. Excellent O3 reference for comparing spatial and temporal distribution.

## Slide 10
Synoptic O3 Comparisons:
EPIC vs. MERRA-2
ΔO3 = EPIC – MERRA-2 | VZA < 69°
﻿ 0.29 ± 2.35% or 0.89 ± 6.70 DU
EPIC O3
MERRA-2 O3
ΔO3

## Slide 11: Validation and Comparison: Volcanic SO2
Validate DVCF SO2 from EPIC, by comparing SO2 mass loading with DVCF SO2 from SNPP OMPS-NM for the same event.

## Slide 12: ﻿SO2 Validation: EPIC vs. SNPP OMPS
June 17, 2018 Eruption of Fernandina, Galápagos Islands, Ecuador

## Slide 13: ﻿SO2 Validation: EPIC vs. SNPP OMPS
June 17, 2018 Eruption of Fernandina, Galápagos Islands, Ecuador
SO2 Mass
SO2 mass agreement better than 10%.

## Slide 14: ﻿SO2 Validation: EPIC vs. SNPP OMPS
SO2 plumes from the eruption of Kilauea volcano, Hawaii
EPIC
OMPS
SO2 mass agreement better than 10%.

## Slide 15: EPIC O3SO2AI Product Accuracy Characterization
O3:
For VZA<69°, EPIC O3 bias low on average by about −1 ± 2.35% or −3.5 ± 6.7 DU.
Volcanic SO2:
Accuracy of individual pixel SO2 (>10 DU) is about 25%
Accuracy mass loading (integrated over SO2 pixels) is about 10%.

## Slide 16: Summary
The O3SO2AI product is released
High accuracy of O3 and SO2 retrievals achieved by applying the DVCF algorithm.
Independent soft calibration, improved algorithm physics, and optimized inversion scheme, all have contributed to the high quality achieved for the EPIC O3SO2AI product.

## Slide 17: New Scheme of O3 Profile Representation: New Column-Classified O3 Profile Climatology
  O3 profile = mean profile + Δprofile
  Δprofile = Σ Ωi eigenvectors
  of covariance matrix

## Slide 18: Algorithm Advances
Any location may be observed with high zenith (SZA and VZA) angles: O3 Profile effect is important.
Direct Vertical Column Fitting (DVCF) Algorithm
Reflection by Earth surface
or by Cloud/Aerosols
Measurement
RT Simulation
O3, SO2
Aerosol Index
M. Error

## Slide 19: DVCF Algorithm
Inversion: Optimal Estimation
All UV bands for profile adjustment
Constraint by measurement errors and parameter uncertainties.
Notes: Multiple wavelengths.